<node type="rviz" name="rviz" pkg="rviz" args="-d $(find tutorial)/rviz/test3.rviz" /><!--2D Navigation-->

How to install the rviz config
firstly, I have to enter
rviz
then
push add, and add map, path , leserscanner , and robot model

then save the config file

25th . Oct 2023

make a branch when we run Subscribers is not good
All subscribers are run simultaneously and each callback judge it call run function or not

Studying Actionlib

cases when someone would like to send a request to a node to perform some task, and also receive a reply to the request. This can currently be achieved via ROS services.

if the service takes a long time to execute, the user might want the ability to cancel the request during execution or get periodic feedback about how the request is progressing

Using Actionlib, the operator get robot feedback information periodically, and cancel the execution
Action aims to handle long-term operation

Action Specification ( Three important components)
Goal, Feedback, Result

Goal: PoseStamped message that contains info about
where the robot should move in the world ,(For controlling the tilting laser scanner, the goal would contain the scan parameters (min angle, max angle, speed, etc). )

Feedback: communication way (type , cycle,etc...)
For moving the base, this might be the robot's current pose along the path. For controlling the tilting laser scanner, this might be the time left until the scan completes.

19th.Oct 2023

1. Do not user spinOnce if I want to a continuous Subscriber
geometr_msgs/Twist, nav_msgs/Odometry

p = n.advertise<geometry_msgs::Twist>("/mobile_base_controller/cmd_vel", 1000);
Subscriber s = n.subscribe("/mobile_base_controller/odom", 1, callback);

void callback(const nav_msgs::Odometry msg)
{
// Write the current pose of the robot from the message to p_current
p_current = msg.pose.pose;

run();
}

void run()
{
ROS_INFO_STREAM("running");

// If the current Position was received for the first time
// the end position is set
if (first_time)
{
first_time = false;

p_end = p_current;
p_end.position.x += 1;
}

if (p_current.position.x < p_end.position.x)
{
// Set x speed to 0.5
twist.linear.x = 0.5;
}
else
{
// Stop the robot
twist.linear.x = 0;

// Publish twist message to the cmd_vel topic of the robot
p.publish(twist);
ROS_INFO_STREAM("published!");
}

If u use C++
you should add the following parts in Cmakelists
include_directories(
# include
${catkin_INCLUDE_DIRS}
)
add_executable(movetask1 src/movetask1.cpp)
add_executable(movetask2 src/movetask2.cpp)
target_link_libraries(movetask1 ${catkin_LIBRARIES})
target_link_libraries(movetask2 ${catkin_LIBRARIES})

task2
Related to TF

ROS uses quaternions to track and apply rotations. A quaternion has 4 components (x,y,z,w).
 That's right, 'w' is last (but beware: some libraries like Eigen put w as the first number!)
The commonly-used unit quaternion that yields no rotation about the x/y/z axes is (0,0,0,1):

The magnitude of quaternion should be one.
In order to avoid the numerical errors that comes to this, you can use
q.normalze()

ROS uses two quaternion datatypes: msg and 'tf.'
geometry_msgs::Quaternion
tf2::Quaaternion

To convert between them in C++, use the methods of tf2_geometry_msgs.

tf2::convert(quat_msg , quat_tf);
// or
tf2::fromMsg(quat_msg, quat_tf);
// or for the other conversion direction
quat_msg = tf2::toMsg(quat_tf);

it is really hard to think the rotation using Quaternion therefore, first you should think it by using RPY then convert Quaternion

To apply the rotation of one quaternion to a pose, simply multiply the previous quaternion of the pose by the quaternion representing the desired rotation.
 The order of this multiplication matters.

First convert pose.orientation to quaternion

tf2::convert(commanded_pose.pose.orientation , q_orig);
Second, generate a quaternion to rotate .
double r=3.14159, p=0, y=0; // Rotate the previous pose by 180* about X
q_rot.setRPY(r, p, y);
Then rotate by multiplying two quaternion- note.. order is important
q_new = q_rot*q_orig; // Calculate the new orientation
q_new.normalize(); // normalize the magnitude

Finally, apply new quaternion to the previous pose
// Stuff the new rotation back into the pose. This requires conversion into a msg type
tf2::convert(q_new, commanded_pose.pose.orientation);

If I know the RPY from quartenion , we can get it by following procedures.
Double roll, pitch, yaw_end
tf2::Matrix3x3 matrix_end(q_new);
matrix_end.getRPY(roll,pitch,yaw_end);

q_new is a quartenion

And debug is really important!!!!!!!!!!!!!
ROS_INFO("running state: %i", state);

to upload git

git add .
git commit -m “message or memo”
git push origin
username is my gmail address
password is my token

task 3
AMCL is a probabilistic algorithm that uses a particle filter to estimate a robot's 2D pose based on sensor data
The task aims to know that there are some way to localize the robot postion. (Odmetory, AMCL, …)

In AMCL, to estimate the robot position the algorithm use Odmetoly data and Lidar sensor data
In AMCL , empty world is NOT suitable because it cannot use sensor information
good point : more precious
bad point : the estimated values are NOT continuous

In Odometory, to estimate the robot position , the algorithm use the rotation of tire and the radious of tire .
Good point: the estimated values are continuous
Bad point : less precious because of the tire slipping and the error of diameter

In grounld truth, this is the answer

to achive this task
1. I have to change the map to use AMCL
2. I have to add 2 more subscriber
Subscriber s = n.subscribe("/mobile_base_controller/odom", 1, callback);

3, I have to change the robot position information
void callback(const nav_msgs::Odometry msg)

this task main theme is to change the robot localization method